## Slide 1: Flooding: what is normal?
Professor Paul Bates
School of Geographical Sciences
http://www.bristol.ac.uk/geography/people/paul-d-bates/

## Slide 2: UK properties flooded per annum
Chart: 
| 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0
Number of residential properties flooded | 4500 | 0 | 10000 | 0 | 0 | 200 | 0 | 2500 | 0 | 55300 | 0 | 1800 | 0 | 0 | 7000 | 0 | 8000 | 16000
Penning-Rowsell, E. C. (2015), A realistic assessment of fluvial and coastal flood risk in England and Wales. Transactions of the Institute of British Geographers, 40: 44–61.

## Slide 3: Changes in high flows over time

## Slide 4: But signal not always so clear

## Slide 5: Why does flooding seem more common?
Changing hazard
  Natural ‘flood rich’ and ‘flood poor’ climate periods
  Super-imposed (but difficult to detect) man-made climate trends
  Catchment changes (urbanisation, changing farming practices)
Changing exposure
  Large numbers of properties built in the floodplain over the post-war period
  250,000 between 2001 and 2014, approx. 12% of all development
  Approx. 23,000 homes since 2001 built in areas of high risk (defined as a 1-in-30 or greater annual chance of flooding)
Changing vulnerability
  Rising incomes have increased the assets at risk
  Losses are proportionately greater, resilience has reduced

## Slide 6: Flood management 101: how big, how frequent?
Return period
Flow
River Avon at Evesham 1961-2008
July 2007
1in 100 = 360m³/s

## Slide 7: Observed uncertainty (5-95% bounds)
Return period
Flow
River Avon
1in 100 = 310 to 425m³/s

## Slide 8: Current best climate projections: UKCIP09
Source: http://www.ukcip.org.uk/

## Slide 9: Future flow projections 2070-2099
Return period
Flow
River Avon
1in 100 = 310 to 580m³/s
Smith, A., Freer, J., Bates, P.D. and Sampson, C. (2014). Comparing ensemble projections of flooding against flood estimation by continuous simulation. Journal of Hydrology, 511, 205–219

## Slide 10: Summary
2015 flooding was ‘normal’
  Extreme where it occurred, absolutely terrible for those affected, but only a 1 in ~3 year national annual loss
We are in a ‘flood rich’ period
  Our (already uncertain) estimates of flow magnitude vs. frequency may be systematically wrong
  But using a shorter record will mean less accurate design flow estimates and much larger uncertainty bounds
Post-war increases in flood exposure have been significant
  And these trends are continuing
  Major driver of increasing risk
Current best evidence suggests climate change will increase flood magnitudes
  But extreme rainfall and decadal flood cycles not well simulated by the UKCIP09 models