## Slide 1
The benefits satellite data can bring to weather forecasting and climate research
Dr Roger Saunders
Head Satellite Applications
Met Office, Exeter

## Slide 2
From Barometers to satellite radiometers
Measuring the Atmosphere
~1643
1995

## Slide 3: Topics
Meteorological satellites
Processing the data
Applications in Weather and Climate
Future Prospects
What
How
Why

## Slide 4: Geostationary Satellites
continual coverage of one section of the globe
data acquisition straightforward
active systems unlikely
large antennas for microwave systems
poor polar coverage
At an altitude of 35,800 km satellite rotates once around the Earth in 24 hours

## Slide 5: Meteosat - the European Geostationary Imager
Scans Africa, Europe, Middle East and Atlantic every 15 minutes
3/1 km spatial resolution at 0° N, 0° E
12 channels (different wavelengths)
Meteosat-10 operational, Meteosat-9 backup

## Slide 6: Polar Orbit
crossing time of the equator is fixed
good polar coverage
good resolution
active systems are viable
larger payloads with more instruments
satellite only views a portion of the earth at one time
Satellite altitudes typically 850 km and pass close to the pole. At a certain inclination to the equator (~98.7º), the satellite's orbital plane will appear to be fixed with respect to the sun (sun-synchronous).

## Slide 7: Metop: The European Polar System (EPS) - will be with us until 2020s
Notes: ASCAT a good example of an ex-research sat instrument now on an operational platform

## Slide 8
Notes: CGMS = Coordination Group for Meteorological Satellites
As its name suggests it is tasked with ensuring coordination between satellite developers & operators in such things as orbits, instruments, distribution methods and inter-agency contingency planning.
The picture shows the situation a couple of years ago – it is a bit idealised and in practice satellite failures rendered it out-of-date and have hence increased the need for an improved global system (eg both the LEO and GEO Russian sats have failed, as has GMS).

## Slide 9: Typical ground track of one polar satellite over six hours
swath width ~2000 km
Orbit period ~100 minutes

## Slide 10: Ground track of five polar satellites over six hours

## Slide 11: c.f. baloon observations used in six hours…
Sonde coverage is more dense over land and NH
Satellite data has largest impact over sea and in SH
where conventional observations are relatively sparse

## Slide 12
Who provides weather satellite data?
EUMETSAT – European Member States (not the same as EU!) based in Darmstadt
NOAA – U.S. Weather Agency was first to provide data since 1970s
Japanese Met Agency/JAXA
Chinese Met Agency
Indian Met Department/ISRO
EUMETSAT HQ, Germany
US-NOAA – Suomi-NPP orbiter

## Slide 13
Other weather satellite data providers
European Space Agency
  Pre-operational satellites
  Research satellites
NASA
  Pre-operational satellites
  Research satellites
European Union
  Copernicus / Sentinels
Commercial Providers ?
  See later

## Slide 14
Operational polar orbiters
US
Europe
China
Notes: This is background information:
Pre-2006 - US (NOAA) satellite programmes have provided the core (and only!) data for NWP and climate studies on upper atmospheric temperature (eg MSU/AMSUA climate trends: Christy et al to Zou et al). There is a large body of work concerned with characterising, and correcting, biases in this data. The work on MSU data is ongoing – 36 years after the first MSU was launched (see Lu and Bell (2014)).
From 2006, Europe has made a contribution to the satellite observing network, with the launch of MetOp-A.
Looking forward, China is set to make an increasing contribution to this constellation of satellite sounders. FY-3A (launched 2008) and FY-3B (launched 2010) were the first experimental missions of the FY-3 polar programme. FY-3C (launched 2013) is the first operational satellite in this series.
FY-3A and FY-3B instruments have been characterised using NWP (see Lu et al 2011a,b,c) These studies have identified a number of issues with the on-orbit performance of the FY-3 instruments & this information has been fed back to CMA-NSMC to guide the design, pre-launch characterisation and on-orbit monitoring of subsequent instruments.
This component of CSSP WP1 aims to extend this support to FY-3C (and subsequent missions).

## Slide 15: Topics
Meteorological satellites
Processing the data
Applications in Weather and Climate
Future Prospects

## Slide 16: Atmospheric sounding of temperature and humidity
2. Satellites: A brief overview
We use different wavelengths to
sound the atmosphere
Microwave radiation mm wavelengths
Infrared radiation 𝜇m wavelengths
Visible/UV radiation nm wavelengths

## Slide 17: Key absorbing gases in the microwave spectral region
3 0.3 wavelength (cm) 0.1
183.31 GHz
22.24 GHz

## Slide 18: Why Use Microwave Frequencies?
Frequency range of 20 – 200 GHz (1cm – 1mm)
Effect of clouds in field of view can generally be neglected
Main absorbers are oxygen and water
Rain in the field of view causes scattering and absorption
  Data screening required
More data usage:
  Infra-red: cloud-free cases ~20% data
  Microwave: use ~90% data

## Slide 19: Microwave sounding data: some examples of measured radiances
50.3 GHz
.
52.8 GHz
53.6 GHz
54.4 GHz
183±1 GHz
183±5 GHz
183±7 GHz
150 GHz
Brightness
temperature
measurements
obtained over
~12 hours
200K
300K
300K
150K
spatial resolution
~25-40 km

## Slide 20: How do we use InfraRed Spectrum?
Temperature Sounding
Temperature Sounding (not currently used)
Water Vapour Sounding

## Slide 21: Atmospheric Motion Vectors

## Slide 22: Assimilated AMVs for one global run

## Slide 23: Active Instruments: Scatterometers

## Slide 24
Backscatter and surface roughness
Incident radiation
Backscattered component
Notes: When sea is like a mirror (Beaufort 0) all the incoming radiation reflects, zero return in direction of incoming signal from scatterometer
As sea roughens, majority of energy reflects off but there is some scattering, including a small amount back in the direction of incoming radiation
As wind speed increases, the sea roughens and the backscatter signal increases.

## Slide 25
Messages for THORPEX
TS Isaac
Became
TS Joyce
Notes: The system on the left is Tropical Storm Isaac (viewed ~1530z) and the system on the right (~1400z) has a very high probability of developing into a tropical storm in the next day or so. See http://www.nhc.noaa.gov/
25

## Slide 26: GPS Radio Occultation
Viewed from the LEO (~800 km) the GPS satellite (~20000 km) is constantly rising or setting behind the Earth’s horizon – “radio occultations.” GPS signals are slightly delayed and their path slightly bent as they pass through the ionosphere and atmosphere. Measurement of this time delay, together with precise computations of the position and velocity of the satellites allows the “bending angle” to be calculated.
Notes: The impact parameter, a, is the distance of closest approach for the straight line path. What we get is a profile of BA as a function of impact parameter.

## Slide 27: How many GPS obs do we get per data assimilation cycle?
Typically ~400 profiles in a 6-hour cycle, with 250-300 observations within each profile
COSMIC mission receivers on 4 satellites (UCAR)
GRAS receivers on Metop-A and –B
TerraSAR-X (GFZ)

## Slide 28: Topics
Meteorological satellites
Processing the data
Applications in Weather and Climate
Future Prospects

## Slide 29
Weather
Climate
Science
Services
Government
Industry
Military
Civilian
International
National
Meteorology
Multi-hazard
£30bn
Services for
Government
Notes: The Public Weather Service uses the core suite of forecast products to provide services to government and public.
Provide tailored services to Defence and Security for strategic and tactical decision making both in and out of theatre.
Model outputs are essential in our services to Civil Aviation, not only nationally but also internationally in our roles as one of the two World Area Forecast Centres and as a Volcanic Ash Advisory Centre.
Services provided in the area of Natural Hazard and Resilience Management through the Natural Hazards Partnership.
Provision of underpinning data for Climate Monitoring and Prediction in providing the climate datasets and validation of climate prediction models.

## Slide 30: Forecasting the weather
du = ∂p – fv
dt ∂x
dv = ∂p + fu
dt ∂y
p = RT
ρ
Risk Analysis & Communication
Knowledge
70 levels
17km
80km high
Forecast Model
Observations
Notes: The raw data to start a forecast are two-fold:
Firstly, our understanding of the atmosphere, encapsulated in the formulation of the model.
Secondly, observations of the recent state of the atmosphere, used to start the forecast.
The forecast model process adjusts the latest estimate of the evolution of atmospheric structure to optimise the fit to recent observations, and then continues the evolution to create the forecast. The model outputs are post-processed to provide an optimal match to the requirements of customers.
Finally the forecast products are used in risk assessment processes to determine the required responses.

## Slide 31: 60 Years of Met Office Computers
Conclusion: x100 increase in computing power every decade

## Slide 32
Seamless Prediction
Essential support to decision making on all timescales
Forecast lead-time
Now
Hours
Days
1-week
1-month
Seasonal
Decadal
Climate
Past climate
Confidence boundary
Analysis of past weather observations to manage climate risks
Eg. Agriculture: informs crop choice, planting to yield optimisation and minimise crop failure risk.
Predicting routine and hazardous weather conditions.
Public, emergency response, international Disaster Risk Reduction
Monthly to decadal predictions - probability of drought, cold, hurricanes….
Contingency planners, national and international humanitarian response, government and private infrastructure investment
Global and regional climate predictions.
Informs mitigation policy and adaptation choices. Impacts on water resources, heat stress, crops, infrastructure.
Notes: The Vuvuzela of seamless prediction:
The Met Office is able to make predictions on all timescales from now until a century ahead.
Analysis of past weather data is also useful to understand weather risks today – for example what is the likelihood of a particular storm event occurring.
On longer timescales the confidence boundary gets wider – however if the climate information is applied in an appropriate manner it provides extremely useful information to inform adaptation decision making.

## Slide 33
An example of simulated imagery from Model
Approx time taken to run forward model for single channel was 4 mins

## Slide 34
Impact of satellite data in NWP
FSOI results showing impact of observations for 24hr forecasts in global model
Notes: This is the most recent set of FSO for 24 hr forecasts for Global results for 6 months

## Slide 35
2 day forecast in 2015 as good as 1 day forecast in 2000
Example: European Area Mean Sea Level Pressure Error
Forecast skill
Global model ‘skilful forecast range’ increasing in line with long-term trend of one day per decade increase in forecast skill (comparing days 2, 3 and 4)
Notes: Verification v analysis for “area 2” (covering the N Atlantic, UK, Iceland and Western Europe), which is defined as a rectangle on a polar stereo-graphic projection. Accuracy has improved to the extent that one day of forecast predictability has been gained approximately every 10 years.
Q: What happened in 2015? Need to look at a) Wider area (this is just Europe) – NH/SH/tropics?, b) Other variables (global NWP improvements driven by e.g. weather rather than PMSL these days? Start with global index parameters, and also weather e.g. T850, surf U/T?), c) Was 2015 particularly unusual (spike in persistence) – note though that we’ve had spikes/dips in the past (e.g. 1999) that didn’t correlate so much with skill decrease, whereas early, late 1980s there is some evidence?

## Slide 36: Gobal Model Performance
Met Office
Global ranking of Met Office Global Model forecast accuracy based on the WMO weighted global index components used by the WMO/CBS
`USA 13km
Europe
9km
UK
German
ICON
* Parameters: Surface pressure, 500hPa geopotential height, 250hPa/850hPa Winds; Forecast ranges from T+24h to T+120h
Skill* Difference (%) relative to Met Office
BoM
40km, DA
Better
Worse

## Slide 37
Benefit to UK: Storm Surge
2013 from BBC web site
The tidal surge which hit the east coast of Britain has been described as the "most serious" for 60 years. But the Environment Agency said 800,000 homes had been protected by flood defences and better forecasting had given people "vital time" to prepare.
1953 wikipedia
2,551 killed (1,836 in the NL, 307 in England, 28 in Belgium, 19 in Scotland, 361 at sea). Very little warning given.

## Slide 38: Satellite Imagery for Hazard Alerts
Aircraft
icing
Snow cover
Fog
Night
imagery
Simulated
imagery
Severe
convection
Cloud
parameters
Dust
Instability
Lightning
Rain
Volcanic
Ash

## Slide 39
Dust RGB
Ash size
Ash column loading
Ash(-top) height
Volcanic Ash Detection from satellites

## Slide 40: Air Asia QZ8501
The Airbus A320 vanished with 162 people aboard en route from Surabaya in Indonesia to Singapore

## Slide 41
9th May 2013, 0800 UTC
WV-IRW BTD + IRW Texture
HRV
Severe Convection RGB
Detected OTs

## Slide 42: Meteosat-9, 26th June 2013, 1330 UTC
Positive OT detections
Crosses – locations of ATD lightning strikes in previous 15 minutes, colour-coded
<3 m 3-6 m 6-9 m 9-12 m 12-15 m

## Slide 43
Climate models are increasing in complexity and resolution
- From AOGCMs to Earth System Models with biogeochemical cycles -
Atmospheric Chemistry
https://www2.ucar.edu/news/understanding-climate-change-multimedia-gallery
130 km resolution orography
25 km resolution orography

## Slide 44: Climate Change Initiative

## Slide 45: Observations for Climate Model Evaluation
How to bring as much observational scrutiny as possible to the CMIP/IPCC process?
How to best utilize the wealth of satellite observations for the CMIP/IPCC process?
CMIP6
Obs4MIPs has defined a set of technical specifications and criteria for developing observational data sets that are technically aligned with CMIP model output (with common file format, data and metadata structure).

## Slide 46: Topics
Meteorological satellites
Processing the data
Applications in Weather and Climate
Future Prospects

## Slide 47
The Future: Doppler Wind Lidar
DWL measures Doppler frequency shift of backscattered light
Scattering from
Air molecules (clear air) – Rayleigh scattering
Particles (aerosol/cloud) – Mie scattering
Atmospheric backscatter from a laser pulse collected by a telescope, range-gated, and spectrally analyzed to determine the Doppler shift. The range gates, Doppler shift, telescope look-angle and satellite orbit can be used to calculate the wind velocity as a function of altitude.
Aeolus-ADM mission
  ESA Earth Explorer Core Mission chosen in 1999
  Technology demonstration, ~3 years
  Launch, Late 2017

## Slide 48
Ground Segment
ISL
ISL
Radio Occultation Measurements
GNSS Constellations
GNSS Reflectometry Specular Point
Cubesats the future?
GNSS Reflectometry
Surface wind/ Sig wave height
Sea-ice cover
Snow water equivalent
Soil moisture

## Slide 49: Funding for European Satellites
PWS funding from: Government,
Civil Aviation and Data Wholesaling

## Slide 50: Funding for European Satellites
PWS funding from: Government,
Civil Aviation and Data Wholesaling
This approach remains the most cost-effective way to satisfy our requirements. The alternatives to engaging with EUMETSAT would be:
A national programme. The UK pays ~14% of the EUMETSAT programmes. A dedicated UK programme, could not reduce the overall cost to this degree.
Purchase of service from elsewhere. There are no other satellite operators able to offer the required capability for the forseeable future.
Purchase of satellites from elsewhere. The cost of the equivalent US weather satellite programme is currently $11.3Bn – roughly double the cost of the European programme. Chinese satellite and Cubesat technology still needs to be proven.

## Slide 51: Wider exploitation of satellite data
Use more of existing satellite data for weather forecasting:
  Over Land, Cloud, polar regions of global model
  Use more spectral channels
  In UK model where cloud/fog forecasting is still a challenge
Improve data assimilation methods and models
Support new services (e.g. air quality, greenhouse gas monitoring, space weather)

## Slide 52
Thanks.
Any Questions?

## Slide 53: Basic facts
Turnover ~£208m (approx 16% Commercial)
People ~2000 Staff
~1400 at Exeter HQ
Locations ~50 manned locations ~Many more unmanned observing sites ~inc 5 permanent and 2 Mobile Met Unit overseas sites
Working areas 37% Forecasting & Observations
28% Science & Research
16% Technology (IT)
12% Commercial and Government Business
7% Corporate Services
Notes: In brief
The Met Office houses the Met Office Hadley Centre – the UK’s leading climate change research centre.
The Met Office is a trading fund within the department of Business, Innovation and Skills – and is required to meet commercial targets.
The Met Office employs over 1,900 people at 50 sites globally.
In full
As a Trading Fund the Met Office is required to operate on a commercial basis and meet agreed performance targets as set by the Ministerial Owner.
Our main sources of income are from:
  Public weather services.
  Defence.
  Commercial.
  Climate change.
  Civil sector services.