## Slide 1: The Cold Economy
“Doing cold better”
Professor Toby Peters
Birmingham Energy Institute
Founder – Dearman Engine Company &
Highview Power Storage
November 2014

## Slide 2: Cold is the Cinderella of the energy debate
In the UK, we estimate
+10% of UK electricity demand being used to meet cold needs (could be as high as 14%)
Around £5.2Bn is spent in the current UK energy system on energy for cooling
(Energy input)
(Heat removed)
Copyright Dearman Engine Company
Notes: From DUKES 2012:
UK primary energy demand = 214.3mtoe
UK natural gas used in power gen = 18.4mtoe i.e. 8.6% of total
Fridge CoP: PERFORMANCE ANALYSIS OF A DOMESTIC REFRIGERATOR, M. Y. Taib, A. A Aziz and A. B. S. Alias 2010

## Slide 3
Copyright Dearman Engine Company
3
Global demand for cooling
The world’s urban population is expected to exceed six billion by 2045, from approximately 3.5bn today
The global middle class is is expected to grow to 4.88bn by 2030 from 1.84bn today

## Slide 4
Copyright Dearman Engine Company
4
Post-harvest food waste
If developing countries had same level of cold chain as UK, they could save 200 million tonnes of perishable food.
$8bn wasted fruit and vegetables in India annually. India produces 11% of the world’s vegetables yet makes up just 1.7% of its vegetable trade.

## Slide 5
Copyright Dearman Engine Company
5
Food waste…a few facts…
Carbon emissions of food produced but not eaten is 3.3 billion tonnes; the third biggest emitter after the US and China
Water consumption of food wastage is 250km3; three times the volume of Lake Geneva
Food wastage occupies 1.4 billion hectares of land, almost 30% of the world’s agricultural land
Almost a quarter (23%) of fertiliser is used to produce food that is never eaten

## Slide 6
Copyright Dearman Engine Company
6
Cold Chain challenge – matching societal demands…
The global cold chain is expected to grow 16% per year in the five years to 2018
Developed countries are seeing 10% growth and developing 25%+
India projects it needs to spend more than $15 billion on its cold chain over the next five years
China’s refrigerated storage capacity is on track to multiply 20-fold to 5 billion cubic feet in the decade to 2017
The global healthcare cold chain logistics market is expected to expand from US$7.3 billion in 2013 to US$11.4 billion in 2018

## Slide 7
Copyright Dearman Engine Company
7
with the environmental impact…
A transport refrigeration unit:
  consumes up to 20% of a refrigerated vehicle’s diesel
  can emit up to 6x NOx and 29x PM of Euro VI engine
  produce significant amounts of C02
  uses HFC refrigerants harmful to the atmosphere
Notes: If current trends in refrigerant usage were to continue, experts project that hydrofluorocarbons would be responsible for nearly half of all global greenhouse-gas emissions by 2050

## Slide 8
Copyright Dearman Engine Company
8
We need to store renewable / waste energy to use on demand in grid or transport applications
Liquid air is about storing cold and power
Not a panacea, but a leapfrog solution linking renewable or wasted energy, including waste cold, to cooling, and power demands
Liquefying air is the cornerstone of the industrial gas industry – existing infrastructure
Harness low-grade waste heat

## Slide 9
Copyright Dearman Engine Company
9
The Dearman Engine
Return Stroke
Warm heat exchange fluid (HEF) enters the cylinder.
Top Dead Centre
Liquid Air injected - comes into contact with the HEF causes rapid temperature rise.
Power Stroke
The now gaseous air expands pushing the piston down. Direct contact heat transfer continues allowing near isothermal expansion.
Bottom Dead Centre
The exhaust mixture leaves the cylinder. The gaseous air is returned to the atmosphere and the HEF is re-heated and re-used.
1
2
3
4

## Slide 10
Copyright Dearman Engine Company
10
Benefits
Made from simple materials in well-established processes
Can use waste heat to boost efficiency, even at low temperatures
Fuel non-combustible, exhaust cool, and clean
Liquid air or N2 widely produced and available
Low capital cost
Fits established manufacturing base
Low life-cycle impacts
Waste heat (i.e. inefficiency) is a problem for engines and fuel cells
Works alongside other technologies rather than seeking to replace them
Synergies with cooling applications
Indoor and underground use possible
Modest infrastructure requirement
Opportunity to integrate at system level with e.g. renewable energy to achieve zero CO2
Characteristics
Advantages
Cheap zero-emission power system – no life-cycle surprises, free cooling

## Slide 11
Copyright Dearman Engine Company
11
Liquid air can be used in different mobile applications…
Engine-based refrigeration
Waste heat recovery engine efficiency
Combined cooling and propulsion
Aux power and air-conditioning

## Slide 12
Copyright Dearman Engine Company
12
Large scale Dearman Engines can be used to provide zero emission and lower CO2 cooling and power on demand (back-up or peak power) for refrigerated buildings, data centre, supermarkets.
…and also stationary applications

## Slide 13
Copyright Dearman Engine Company
13
Clean energy solutions need to make a significant commercial case (economics / license to operate)
Cheaper and cleaner refrigerated transport or air conditioning
A transport refrigeration unit consumes 15-20% of a refrigerated vehicle’s diesel, and emits up to 29 times as much PM and 6 times more NOx than a modern Euro VI primary diesel engine
High efficiency waste heat recovery system. Harnessing waste heat of the radiator loop, saving upwards of 25% diesel consumption
UK case | Vs Diesel
CapEx | +£270
Yearly OpEx | -£1,200
Payback Time | ~2 months
10yr TCO | -£12k
UK case | Bus with a/c
CapEx | +£4,000
Yearly OpEx | -£2,800
Payback Time | < 1.5 years
10yr TCO | -£24k

## Slide 14
 | Distance . miles to nearest plant | Available daily resource
London | 48 | 180
Leeds | 23 | 365
Glasgow | 16 | 140
Sheffield | 6 | 365
Bradford | 33 | 365
Manchester | 9 | 140
Edinburgh | 36 | 140
Liverpool | 13 | 140
Cardiff | 30 | 350
Wakefield | 25 | 225
Nottingham | 41 | 225
Newcastle | 46 | 220
Sunderland | 35 | 220
Hull | 5 | 140
Stoke-on-Trent | 37 | 140
Derby | 44 | 225
Swansea | 12 | 350
Southampton | 13 | 350
Portsmouth | 36 | 350
Oxford | 14 | 360
Liquid air supply is well understood and widely available in industrial markets

## Slide 15
Copyright Dearman Engine Company
15
Stage of development
Transport refrigeration in on-vehicle demonstration, field trials next year and manufacture from 2016
Waste-heat hybrid for bus/trucks in demonstration next year
Aux Power Unit and static peaking / reserve plant in development (subject of grant funding applications)
Birmingham Centre for Cryogenic Energy Storage and LAES pilot demonstrator
5MW liquid air energy storage system in operation next year
  $60M+ of UK Government, industry and international private investor funding to date

## Slide 16
Copyright Dearman Engine Company
16
The Cold Economy – a systems approach to cooling
The scale and importance of cold is not reflected in the way in which it is represented when future energy needs are quantified
Cold demands are embedded in final energy demands for various sectors
We do not think about waste cold

## Slide 17
Copyright Dearman Engine Company
17
Existing LNG regasification capacity is significantly under-utilised
Source: GIIGNL, The LNG Industry in 2013
Global LNG regasification capacity & utilisation
  2013 study of 83 LNG terminals found 25 terminals exploiting 38 “cold synergies”

## Slide 18
Copyright Dearman Engine Company
18
Liquid air can serve as an intermediary between cold sources and needs
Liquid air de-couples the requirement for cold sources and needs to coincide…
  Spatially – liquid air can be transported to dispersed locations
  Temporally – liquid air can be stored until needed
Liquid air also brings flexibility as it can find uses in multiple static and transport cooling applications
Warehouses
Bus depots
Isle of Grain

## Slide 19
Current primary energy consumption to deliver cold is around 52TWh – utilising all of current exploitable resource would achieve 22% reduction in primary energy inputs for cold
In theory 2030 resource could achieve 85% reduction although this is almost impossible in practice
Future exploitable resource could be as high as 86TWh

## Slide 20: An integrated UK cold energy system would allow for reductions in primary energy demand, saving £1.1Bn

## Slide 21
Global opportunity

## Slide 22
Copyright Dearman Engine Company
22
The Cold Economy - An integrated solution
Integration of waste cold & sources
Liquid air in transport refrigeration
Renewables (off-grid & ‘wrong-time’)
Efficiency improvement (operational & technical)
Co-location of multiple demands
Exploitation of waste heat

## Slide 23: The Cold Economy is based on an efficiently integrated Cold Energy System
A Cold Energy System is an energy system that correctly represents cold flows and their integration
The Cold Economy represents the value and opportunities (business, environmental etc.) created by implementation of an efficiently integrated Cold Energy System
Features of the Cold Economy include:
  Greater integration between waste cold resources and cold needs
  Liquid air and other cryogens as a means of storing cold and meeting cold needs
  Use of more efficient technologies, materials and practices for meeting cold needs
  An energy system view that incorporates cold flows
Benefits of the Cold Economy include:
  Meeting cold needs in a more resource efficient way
  Spatial & temporal balancing of dynamic needs
  Environmental benefits including reduced GHG emissions and improved local air quality
  Lower overall cost & new business opportunities and jobs for UK plc

## Slide 24
Copyright University of Birmingham and Dearman Engine Company 2014

## Slide 25
Copyright Dearman Engine Company
25
…from a garden shed in Bishop’s Stortford, UK
Liquid air – a global solution to clean cold and power.
For further information, please contact:
Professor Toby Peters
toby.peters@dearmanengine.com
Asst: Jess Lingwood
jessica.lingwood@dearmanengine.com
T: 0203 617 9170