## Slide 1: Energy storage innovation: technology + policy
Dr Jonathan Radcliffe
University of Birmingham & Centre for Low Carbon Futures

## Slide 2: Energy storage technologies
Hot water cylinder: one tank = 6kWhth; 14m tanks = 84GWhth
Pumped hydro storage:
total UK = 28GWhe
Coal: 1Mt coal = 3,000 GWhe (about two months output at 2GW)

## Slide 3: Decarbonising power
Sources: UK Energy in Brief (DECC, 2014), UK Renewable Energy Roadmap (DECC, 2009)
Chart: UK progress to 2020 renewables target
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Onshore wind | 9.225 | 8.5782 | 32.5106 | 217.4304 | 343.5011 | 392.3022 | 487.7168 | 666.9844 | 876.8616 | 850.1692 | 944.928 | 960.1443 | 1251.2434 | 1275.5057 | 1736.3943 | 2501.1861 | 3573.6511 | 4491.2823 | 5788.0217 | 7529.3198 | 7135.8523 | 10346.5216 | 12111.658 | 16992.1304 | 34150
Offshore wind | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.9 | 4.9419 | 4.781 | 9.844 | 198.6809 | 402.7057 | 651.4015 | 782.5352 | 1335.3995 | 1753.8947 | 3043.7049 | 5125.8243 | 7549.0545 | 11441.4728 | 44120
Shoreline wave / tidal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0229 | 0.051858 | 0.026001 | 0.034518 | 0.02977 | 0.005 | 0.0172 | 0.036211 | 0.62516 | 1.8387 | 0.9369 | 3.5718 | 5.8878 | 3950
Solar photovoltaics | 0 | 0 | 0 | 0 | 0 | 0.074 | 0.13967 | 0.20534 | 0.271 | 0.67 | 1.2675 | 1.82 | 2.6975 | 2.9445 | 4.0052 | 8.175 | 10.695 | 14 | 17 | 20.0002 | 40.1333 | 244.3437 | 1350.6306 | 2035.6406 | 2240
Hydro | 5206.5689 | 4623.916 | 5431.38 | 4301.752 | 5093.752 | 4837.582 | 3392.21 | 4168.667 | 5117.252 | 5335.7734 | 5085.2528 | 4055.7094 | 4787.9203 | 3137.5086 | 4843.9549 | 4921.4828 | 4593.0677 | 5077.3034 | 5144.8468 | 5230.566 | 3567.6163 | 5682.2254 | 5284.6951 | 4698.0602 | 6360
Bioenergy | 595.8255 | 687.9018 | 934.1881 | 1197.9518 | 1518.455 | 1641.5711 | 1804.5743 | 2109.7862 | 2654.2419 | 3429.1167 | 3881.8221 | 4526.0381 | 5080.1256 | 6173.7139 | 7363.8779 | 9102.2989 | 9276.8742 | 9324.5012 | 9534.6068 | 10673.6396 | 11996.2956 | 13098.1685 | 14914.2937 | 18493.7433 | 26160
Notes: Shows indicative amounts of capacity for 2020, against that which installed to date

## Slide 4: Electrifying space heat
Current gas storage ̴50,000 GWh
Generation capacity to meet all electrical space heat demand in 2030 (if a smooth distribution) would be ̴10GW.
Meeting spikes from weather and evening peak demand could double this.
LDZ
offtakes
NTS power stations
NTS industrials
Gas demand, excl. interconnectors and storage

## Slide 5: UK Energy system need for flexibility
Timescale | Challenge
Seconds | Renewable generation introduces harmonics and affects power supply quality. Reduced inertia from less rotating machinery.
Minutes | Rapid ramping to respond to changing supply from wind/PV generation.
Hours | Daily peak for electricity is greater to meet demand for heat and EV.
Hours - days | Variability of wind generation.
Months | Increased use of electricity for heat leads to strong seasonal demand profile.

## Slide 6: Electricity Storage Technology options
 |  | Reserve & response services | Transmission & distribution grid support | Bulk power management
Discharge time at power rating | Hours |  |  | 
 | Minutes |  |  | 
 | Seconds |  |  | 
 |  | 1kW 10kW | 100kW 1MW 10MW | 100MW 1GW
Pumped hydro storage
High Power Supercapacitors
Superconducting magnetic energy storage
Flywheels
Hydrogen Fuel Cells
Compressed Air Energy Storage
Li-ion batteries
Advanced lead-acid batteries
High Energy Supercapacitors
Sodium sulphur batteries
Flow batteries
Advanced lead-acid batteries
Nickel-Cadmium batteries
Nickel metal hydride batteries
Liquid Air Energy Storage
Thermal
Electrochemical
Mechanical
Electrical
Chemical

## Slide 7: Technology innovation
One of the Government’s ‘Eight Great Technologies’
Energy storage has “the potential for delivering massive benefits – in terms of savings on UK energy spend, environmental benefits, economic growth and in enabling UK business to exploit these technologies internationally.”
Support from
Research Councils: Capital equipment + programme funding
Innovate UK (TSB): Energy Catalyst, Catapult etc.
Energy Technologies Institute: invested in Isentropic, pumped heat storage
DECC: demonstration programme
Ofgem: Network Innovation Competition
EU: Horizon 2020

## Slide 8: A technology: liquid air
710lts air
1lt Lair
stored at
atmospheric pressure
710lts air + lots of cold
Waste / off-peak electricity
Power
on-demand
-196 C
Harness
low grade
waste heat
Highview Power Storage
DECC funding 5MW/3 hour demo on landfill gas power plant
Birmingham Centre for Cryogenic Energy Storage
£5.9m EPSRC + £1.2m institution + £5.2m industry
300kW grid-connected pilot plant being sited at UoB

## Slide 9: Overcoming barriers to deployment
Technology cost and performance: other technologies are currently cheaper
Uncertainty of value: the future value is dependent on the energy system mix
Business: capturing multiple revenue streams is difficult to establish, both for a potential business and the market in which it will operate
Markets: the true value of energy is not reflected in the price; more fundamentally, the future long-term value of storage cannot be recognized in today’s market
Regulatory/policy framework: restrictions on ownership; paying levies twice
Societal: wider community acceptance has not yet been considered

## Slide 10: Conclusions
Energy storage could play an important role in a cost-effective transition to low carbon, resilient energy system (globally)
Technologies exist which can respond to energy system challenges, their value will increase, costs will reduce
However, short-term fixes could crowd the market for more efficient long-term solutions
Support needs to be well coordinated and strategic, across the innovation process, research to deployment
Think whole system: electricity/heat/cold
Innovative policy & regulation needed to provide a market through which value (of flexibility) can be accessed
Raises prospect of new business models for energy