## Slide 1
Climate Change: Is there a Plan B?
Parliamentary and Scientific Committee
Hugh Hunt
@hughhunt hemh1@cam.ac.uk
Cambridge University Engineering Department
October 2019

## Slide 2
How well is “Plan A” working?
Fossil fuel use
rising
Population
rising
Energy use per capita
rising*
CO2 per kWh
falling slowly*
* we are relying too much on technology to bring these down.
What about behaviour?

## Slide 3
Arctic summer ice area : a good indicator

## Slide 4: The Arctic problem
Arctic ice yielding to open water, albedo (reflectivity) drops from 0.6 to 0.1
Albedo loss from summer ice has the same warming effect as past 25 years of CO2 emissions.
Arctic Ocean is shallow, surface warming extends to seabed, melts permafrost, triggers release of methane.
Methane is 20-80 times more potent a GHG as CO2
Greenland ice shelf holds 2million km3 of ice. If it melts → sea-level rise of 7.2m
Ice-free arctic will alter jet stream patterns and ocean circulations → changes in climate

## Slide 5: The Arctic problem
Arctic ice yielding to open water, albedo (reflectivity) drops from 0.6 to 0.1
Albedo loss from summer ice has the same warming effect as past 25 years of CO2 emissions.
Arctic Ocean is shallow, surface warming extends to seabed, melts permafrost, triggers release of methane.
Methane is 20-80 times more potent a GHG as CO2
Greenland ice shelf holds 2million km3 of ice. If it melts → sea-level rise of 7.2m
Ice-free arctic will alter jet stream patterns and ocean circulations → changes in climate

## Slide 6: The Arctic problem
Arctic ice yielding to open water, albedo (reflectivity) drops from 0.6 to 0.1
Albedo loss from summer ice has the same warming effect as past 25 years of CO2 emissions.
Arctic Ocean is shallow, surface warming extends to seabed, melts permafrost, triggers release of methane.
Methane is 20-80 times more potent a GHG as CO2
Greenland ice shelf holds 2million km3 of ice. If it melts → sea-level rise of 7.2m
Ice-free arctic will alter jet stream patterns and ocean circulations → changes in climate

## Slide 7: The Arctic problem
Arctic ice yielding to open water, albedo (reflectivity) drops from 0.6 to 0.1
Albedo loss from summer ice has the same warming effect as past 25 years of CO2 emissions.
Arctic Ocean is shallow, surface warming extends to seabed, melts permafrost, triggers release of methane.
Methane is 20-80 times more potent a GHG as CO2
Greenland ice shelf holds 2million km3 of ice. If it melts → sea-level rise of 7.2m
Ice-free arctic will alter jet stream patterns and ocean circulations → changes in climate

## Slide 8: Global annual CO2 emissions – 35 billion tonnes
35 billion tonnes/year
World pop = 7billion
Global average 5 tonnes/person/yr
My trash: 500kg/yr ?

## Slide 9
Arrival in Melbourne – how much CO2 is my fair share?

## Slide 10
Imagine that each white suitcase contains 20kg of CO2

## Slide 11
A Boeing 747 burns fuel at 4kg per second

## Slide 12
to Melbourne is a 20 hour flight

## Slide 13
There are 350 passengers

## Slide 14
1kg fuel generates 3kg CO2 (carbon + oxygen from air)

## Slide 15
Nsuitcases = 4 x 3 x 20 x 3600 / 350 / 20 = ???

## Slide 16
My share of CO2 for a flight to Melbourne is 2.5 tonnes

## Slide 17
OK – so what are our options ?

## Slide 18: GEOENGINEERING – active control of climate
35 billion tonnes/year
World pop = 7billion
Global average 5 tonnes/person/yr
Return flight to Melbourne 5 tonnes/person
rule of thumb for Air travel:
100kg CO2 per hour of flying
Industrial growth 
Geoengineering ?? 
Net zero
by 2050 ?

## Slide 19
Steep mitigation is impossible.
Large-scale “Negative Emissions” required
ie suck CO2 out of the atmosphere.
NETs = Negative Emissions Technologies
CCS = Carbon Capture and Storage
BECCS = Biomass Energy with CCS
DAC = Direct Air Capture
But the SCALE required is eye-watering.

## Slide 20
Geoengineering:
BECCS = Bio-Energy with Carbon Capture and Storage
(NETs Negative Emissions Technologies)
Implicit in Paris COP21 Agreement

## Slide 21
Geoengineering:
CDR = Carbon Dioxide Removal
BECCS = Bio-Energy with Carbon Capture and Storage

## Slide 22
Geoengineering:
SRM = Solar Radiation Management
CDR = Carbon Dioxide Removal
BECCS = Bio-Energy with Carbon Capture and Storage

## Slide 23: SRM – eruption of Mt Pinatubo, 1991

## Slide 24
Tethered balloon – height 20km maybe 10 balloons worldwide each delivering 30kg/s of aerosol
10m tonnes p.a. for 2 oC cooling ? ? ?
20km optimum height ?
mid-latitude ?
Image: Peter Davidson Technologies
OPTIONS:
- Aircraft
- Airships
- Missiles
- Artillery
- Towers
- Tethered balloons
SPICE: aerosol delivery system for 2oC cooling
Stratospheric Particle Injection for Climate Engineering

## Slide 25: Particle delivery – costs & timescales (target: 10 million tonnes per year )

## Slide 26: SPICE “cancelled” ? Controversial?

## Slide 27: Other SRM: Marine-Cloud Brightening
Spray sea water into clouds to increase reflectivity

## Slide 28
Centre for Climate Repair @ Cambridge (Sir David King)
Iron Salt Aerosol ISA

## Slide 29: Is there a Plan B ?
Yes (SPICE)
Yes
No
Maybe
Hmmm

## Slide 30
Thank you!
hemh1@cam.ac.uk
www.hughhunt.com
@hughhunt
www.suggr.co.uk